## Slide 1
Agent-Aware
Networking
Traffic classification and QoS inside a programmable switch
P4
Research prototype presentation
BMv2 | Mininet | Ryu
Notes: Frame the project as a forwarding-path experiment, not a bot blocker.
The switch infers a service class and applies transport treatment without terminating TLS.
Source: requirements.md sections 1 through 6.

## Slide 2
The congestion problem
02
One human flow shares a queue with a machine-paced burst
human
agent 1
agent 2
agent 3
agent 4
agent 5
shared
queue
tail latency spike
Port 443 and valid TLS make the flows look alike to conventional policy.
Problem statement: encrypted human and agent flows contend at the same bottleneck
Notes: Use the queue drawing to explain the p99 failure mode.
Avoid repeating broad novelty claims. July 2026 Internet-Drafts propose explicit agent identity tied to QoS.
Our claim-safe distinction is behavioral inference in the forwarding path without cooperative identity.

## Slide 3
System architecture
03
Traffic sources
Human traffic
Agent frameworks
Background load
BMv2 switch
PARSE
Ethernet, IP, TCP, TLS
FEATURES
bounded flow state
CLASSIFY
range match tree
ACT
queue, DSCP, ECN, meter
MCP and web target
Ryu controller
policy install
slow-path refinement
state aging
traffic
forward
refine
Frozen interfaces: design.md section 4
Notes: Walk left to right. All per-packet decisions stay in the switch.
The controller refines state and installs policy. Uncertain traffic follows the fail-open path.
Source: design.md sections 3, 4, and 7.

## Slide 4
Traffic classes and treatment
04
CLASS
MEANING
NETWORK TREATMENT
HUMAN_INTERACTIVE
Browsing and video-call-like traffic
Protected queue
AGENT_INTERACTIVE
Latency-sensitive MCP tool calls
Good service with bounded share
AGENT_BULK
Crawling, batch work, scraping
Lowest priority and shaped first
UNKNOWN
Insufficient or uncertain evidence
Best-effort fail-open path
Only AGENT_BULK may drop on meter red. Classification uncertainty never blocks traffic.
Notes: Stress that the policy has three meaningful traffic classes plus UNKNOWN.
Interactive agent traffic receives good service. The system does not equate all agents with abuse.
Source: common/contracts.py and design.md section 4.

## Slide 5
Per-packet pipeline
05
1
Parse
Headers and bounded TLS metadata
2
Update
Saturating fixed-point features
3
Classify
Compiled decision-tree ranges
4
Treat
Queue, marking, ECN, and meter
Invariant
Flow uncertainty degrades to UNKNOWN and best effort. It never becomes an access-control verdict.
Arithmetic and state rules follow design.md section 7
Notes: The data plane uses bounded state and shift-based fixed-point arithmetic.
Every uncertain parser, feature, and classification path must preserve forwarding.
Source: design.md sections 4.2 and 7.

## Slide 6
Experiment matrix
06
375 immutable cells
Five systems × five agent shares × three burst presets × five seeds
Chart: 
| Ours | FIFO | DiffServ | Fair queue | App limiter
Configured cells | 75 | 75 | 75 | 75 | 75
Agent share
10, 30, 50, 70, 90%
Burst
low, med, high
Seeds
1, 2, 3, 4, 5
Predeclared anchors
at least 30% lower human p99 | under 5% added per-packet latency
This chart shows configured run counts, not experimental outcomes.
Notes: The only chart in this draft reports configuration coverage.
Do not present the anchors as achieved until anchors.json verifies both checks from audited artifacts.
Source: eval/configs/*burst_sweep_v1.yaml and requirements.md section 8.

## Slide 7
Centerpiece demo scenario
07
System OFF
System ON
human flow
agent storm
human p99 rises
human flow
agent storm
human p99 stays flat
The dashboard must agree with offline matched two-tap metrics before the demo counts as evidence.
Conceptual timeline. Replace only with audited live data after Linux execution.
Notes: This slide is a conceptual demo storyboard, not a result.
During a real rehearsal, show the live dashboard and archive the raw telemetry, labels, and recording.
Source: harness/demo.py, dashboard/server.py, and docs/demo_rehearsal.md.

## Slide 8
Evidence chain
08
CONFIG
SHA-256 identity
and explicit seed
>
RUN
exclusive host lock
and append-only path
>
ARTIFACTS
two taps, labels,
target timings
>
AUDIT
manifest hashes
and coordinate checks
>
CLAIM
confidence interval
and anchor status
A failed run stays visible. A missing digest blocks aggregation.
This boundary prevents dry runs, fixtures, and edited telemetry from becoming paper numbers.
Evidence rules: design.md sections 7.18 through 7.20
Notes: Explain the chain as the project's central reproducibility control.
The aggregate command rejects incomplete coordinates and artifacts whose hashes no longer match.
Source: eval/run_experiment.py, eval/aggregate.py, and eval/anchors.py.

## Slide 9
Current implementation status
09
Repository ready
Runtime evidence pending
Topology and persistent storm lifecycle
Four baselines and 375-cell configs
Metrics, dashboard, plots, and audit gates
MAWI provenance and replay manifest
Linux BMv2 and Mininet executions
Real captures from four agent frameworks
Authorized CAIDA trace access
Anchor results and two full rehearsals
No experimental performance claim appears in this deck before audited results exist.
Status reflects the repository as of 9 October 2026
Notes: Keep this status slide until the Linux execution evidence exists.
The current macOS host has no active Docker daemon, p4c, Mininet, tcpreplay, or tshark.
Source: docs/notebook.md and eval/preflight.py.

## Slide 10
Demo readiness gate
10
A successful rehearsal must leave evidence
Fresh Linux VM and recorded toolchain commits
System OFF and ON runs with identical coordinates
Live dashboard cross-checked against offline metrics
Archived manifests, pcaps, hashes, logs, and recording
Clean shutdown with no orphan processes
2
complete
rehearsals
required
If the live path fails, show the archived rehearsal and disclose the current failure.
Runbook: docs/demo_rehearsal.md
Notes: End with the evidence standard, not an unverified result.
The fallback recording may only come from a successful archived rehearsal.
Source: docs/demo_rehearsal.md.